## Slide 1: Tortilla Chips
Monoj K Gupta
M G Edible Oil Consulting, Int’l Inc.
2526 204th Street SW, Lynnwood, WA – 98036
Telephone: 972 234 1634
E-Mail: mgupta@sbcglobal.net
Web Site: www.mgedibleoil.com
TCI Convention, Orlando, Dec 6-7, 2018

## Slide 2: How Important is the Tortilla Chips Business in USA?
Expected 2018 Sales……………… >$5,000,000,000.00
Average Growth over Past 5 Years ... 2.4–6 %

## Slide 3: Types of Tortillas
Corn
White Flour
Other Flours
Variety of Grains
In-and-out Seasonal Types

## Slide 4: Perceived Trend in Tortilla Chips Industry
Nutrition
  Higher protein
  Nutritious grains
  Nutritious vegetables
Novelty
  Flavor components in the dough
  Fruits
  Flour from fruits and roots

## Slide 5: Top Tortilla Brands in USA in 2017
Brand | Sales (m $) | Change (%) | Volume (m lbs.) | Change (%)
Doritos | 1,483.3 | +4.5 | 1,094.2 | +1.9
Tostitos | 612.1 | -0.8 | 340.2 | +2.4
Tostitos Scoops | 438.4 | +0.7 | 156.6 | -1.1
Private Label | 263.4 | +12.2 | 94.0 | +1.3
Santitas | 245.3 | +4.0 | 115.5 | +15.5
On the Border | 181.4 | +20.5 | 87.5 | +5.0
Barcel Takis Fuego | 153.4 | +50.5 | 61.9 | +20.6
Mission | 72.4 | -30.3 | 35.2 | +49.8
Calidad | 59.4 | -22.1 | 26.6 | -31.4
Tostitos Simply | 36.3 | +56.1 | 27.1 | -19.7

## Slide 6: Next 10 Brands of Tortilla Chips
Brand | Sales (m $) | Change (%) | Volume (m lbs.) | Change (%)
Food Should Taste Good | 31.0 | -12.7 | 4.1 | -17.4
Garden of Eatin Blue Chips | 29.5 | -4.9 | 6.2 | -6.9
Xochitl | 27.4 | -9.2 | 5.4 | -10.8
Doritos Sabritas Dinamita | 26.7 | +30.3 | 5.7 | +24.6
Late July Organic | 26.3 | +71.6 | 4.2 | +73.3
Doritos Jacked | 25.9 | -26.9 | 5.3 | -30.8
Garden of Eatin | 25.7 | +2.3 | 5.0 | +0.5
Juanita’s | 25.4 | +9.5 | 10.5 | +11.3
Doritos Sabritas | 17.4 | +10.9 | 3.7 | +6.0
Old Dutch | 15.9 | -9.4 | 4.8 | -8.6

## Slide 7: An Attractive Business
One can see the importance of Tortilla Chips Segment in snack food business
  Large volume ($)
  Expanding market
  Emphasis on nutrition
This makes “High Product Quality” a “Necessity”

## Slide 8: What is Good Product Quality?
This is judged by consumers on the basis of:
Acceptable Fresh-Product Traits
Acceptable Product Traits as Consumed

## Slide 9: Fresh-Product Traits
Acceptable fresh product traits are typically judged by the consumers on the basis of
    Flavor
    Color
    Texture
    Overall Appearance
    Aroma
    Oily Taste
    Aftertaste

## Slide 10: Product Traits as They Are Consumed
The product must satisfy the consumers on all of the traits listed on the previous slide
In addition, the product must not be:
    Stale, or
    Rancid
In other words, the product must have good shelf life

## Slide 11
Shelf Life versus Code Date
The product is as good
as fresh on the last date
printed on the bag
Acceptable to consumers on the last date printed on the bag
        Shelf Life of the product is determined through storage study, consumer tests plus identification and quantification of the markers of flavor that affect the product acceptability. This is done through Chemical Analysis
Code date is dictated by
the Sales and Distribution
The realistic code date
on a product must be
Established through proper
Shelf life test of the product

## Slide 12
Indications for Product Shelf life Loss or Failure
Product Texture
  Loss of product crispness
Product Flavor
  Loss of good flavor
  Development of stale flavor
  Development of “off flavor”
  Development of rancid flavor

## Slide 13
Reasons for the Loss of Texture
The product loses texture or becomes less crisp due to moisture gain during storage
Reasons for Moisture Gain
  Using packaging material with low moisture barrier property
  Poor packaging seals
  Damage caused to the packaging during handling
  Storage of the product under high temperature and humidity

## Slide 14: Progression In Product Flavor©
Good Flavor
Loss of Good Flavor
Develop -ment of No Flavor
Development of Off Flavor
Development of Rancid Flavor

## Slide 15: Stale Flavor
Stale flavor is developed due to starch retrogradation
Salty snack foods are low moisture products. They do not exhibit starch retrogradation
Staleness is observed in baked products, such as biscuits, crackers, bread, cakes, donuts, etc
Consumers tend to use the term “staleness” with the “loss of flavor” in the product
A product can be considered “stale” by many consumers at the on-set of the “loss of flavor” of the product

## Slide 16: Off-Flavor/Rancid Flavor
Off-flavor and Rancid flavor are caused mainly by the Oxidized Oil in the product
Off-flavor can be caused by hydrolytic rancidity, found in product fried in coconut oil
Depending on the Degree of Oil Oxidation, the product can exhibit:
    Off Flavor/Oxidized flavor
    Unpleasant after-taste
    Pungent smell or astringent taste
    Rancid flavor
There are two known types of Oil Oxidation:
    Autoxidative
    Photooxidative

## Slide 17: Source of Oxidized Oil
One must not think that the frying oil is the only source of oxidized oil in the product
Some ingredients contain small amounts of oil that are naturally present (Oat Meal, Corn Flour, Wheat Flour, etc.)
This oil can be rancid even in the fresh ingredient when the product is made
This can lead to product rancidity in storage

## Slide 18: Oil Breakdown
    Oil breakdown occurs in various places
      Oil manufacturing, storage and shipping
      Fresh oil receiving and storage at the end-user
      Fryer
      Used oil storage tank (Holding tank)
      Product during storage

## Slide 19: Modes of Oil Breakdown
The oil breaks down through:
Hydrolysis
Autoxidation
Photooxidation
Thermal decomposition

## Slide 20: Hydrolysis
Triglyceride +
Water
Diglyceride +
1 Molecule of Free Fatty Acid
Diglyceride +
Water
Monoglyceride +
2 Molecules of Free Fatty Acid
Conditions Required for Hydrolysis
Oil
Water
+
Must be
in Complete Solution
Oil
Water
+
Do Not Mix
Oil
Water
Surfactant
Oil & Water form a Solution
And the Oil Hydrolyzes

## Slide 21
Sources of Surfactants in Refined Oil
Phospholipids
Soap from Oil Refining
Calcium
Magnesium
Monoglycerides
Diglycerides
Poor Sanitation

## Slide 22
A Layer of Soap Floating on Fryer Oil

## Slide 23: To Minimize Hydrolysis in Fresh Frying Oils
● Phosphorus | <0.5 ppm Not>1.0 ppm
● Calcium | <0.2 ppm Not>0.5 ppm
● Magnesium | <0.2 ppm Not>0.5 ppm
● Sodium | <0.2 ppm Not>0.5 ppm
● Diacylglycerides | <1.5%
● Monoacylglycerides | <0.4%

## Slide 24: Requisites for Autoxidation
Unsaturated Fatty Acids
Heat
Oxygen
Metal Ion (Iron)

## Slide 25
Unsaturated Fatty Acids
+
Metal Ion (Iron)
Free Alkyl Radical
Free Alkyl Radical
+
Oxygen
Peroxy Radical
Peroxy Radical
+
Unsaturated Fatty Acids
Hydroperoxide
+
Free Alkyl Radical
Autoxidation

## Slide 26
● PV | Not>1
● pAV | <3.0 Not>5
● Iron | <0.1 ppm Not>0.3
● Conj. Dienes | <0.5%
● Polars | <2.0% Not>4%
● Polymers | <1.5%
Linolenic Acid | < 2%
To Minimize Autoxidation in Fresh Frying Oils

## Slide 27: Sources of Free Radical
Free radicals are formed whenever oil containing unsaturated fatty acid and containing minute amounts of metal (Iron, Fe) is heated
This can happen in:
  Oil processing
  Frying operation (Abusive Frying Conditions)
      Higher than normal frying oil temperature
      Hot oil in the fryer with no feed
      Reduced rate of fryer throughput
      Frequent fryer ups and downs
      Lack of oil filtration and fryer cleaning

## Slide 28: Sources of Free Radicals
In Oil Processing
Heat
UnsaturatedFatty Acids
Iron (Fe)
Abusive Frying Conditions
High Oil Temperature
Hot oil with No Feed
Reduced Fryer Throughput
Frequent Fryer Shutdowns
No Oil Filtration

## Slide 29
AERATION
FOOD
oxygen
OXIDATION
hydroperoxides
conjugated dienes
FISSION
alcohols
aldehydes
acids
hydrocarbons
ABSORPTION
SOLUBILIZATION
colored compounds
food lipids
VAPORIZATION
steam
volatiles
antioxidants
STEAM
FFA's
digycerides
monoglycerides
DEHYDRATION
dimers
trimers
epoxides
alcohols
hydrocarbons
HEATING
dimers
cyclic compounds
HYDROLYSIS
FREE
RADICALS
Multitude of Reactions Occur in the Oil During Frying
Oxidation
Further Oxidation
Polymerization
Hydrolysis
Further Oxidation
SOURCE: C. W. FRITCH JAOCS, 1983

## Slide 30: Oil Turnover Time
Fryer Oil Turnover Time = No. of Hours required by the Product to remove all of the oil from the Fryer–System. This includes the fryer, the piping and all associated accessories
Desired Oil Turnover Time for
Tortilla Chip fryer = 7 Hrs.Max.

## Slide 31: Fryer is a Chemical Reactor

## Slide 32: Oil Turnover Time Calculation
Example
Total Oil Volume 250gal
1 U S gallon og oil 7.6lb.
Total oil 500 X 7.6 1900lb.
Product throughput 1200lb.hr.
Oil content of the product 25%
Oil carried out by product 1200 X 0.25 300lb.
Oil Turnover Time 1900/300 6.33hr.
Oil Turnover Time at Zero Product Output
= 1900/0 = INFINITY

## Slide 33: Benefits of Modified Composition Oils
The Modified Composition Oils have low Linolenic Acid and Higher Oxidative Stability
The oils also show less polymerization in normal frying

## Slide 34
Fatty Acid (%) | Garden Variety |  |  | Garden Variety |  |  |  | Modified Composition Oils |  |  |  |  | 
Fatty Acid (%) | Soybean | Canola | Sunflower | Cotton | Corn | Palm | Olive | HOSO |  | HO Canola |  | Nu-Sun | HO Sun
 |  |  |  |  |  |  |  | Vistive Gold | Plenish | 75% | 65% |  | 
Saturates | 15 | 7 | 12 | 27 | 13 | 50 | 15 | 6 | 12 | 7 | 8 | 9 | 9
Oleic | 23 | 61 | 16 | 19 | 29 | 39 | 75 | 72 | 75 | 74 | 67 | 65 | 82
Linoleic | 54 | 21 | 71 | 54 | 57 | 10 | 9 | 16 | 16 | 14 | 21 | 26 | 9
Linolenic | 8 | 10 | <1 | <1 | <1 | <1 | - | <3 | <1 | <5 | <3 | - | -
M. K. Gupta,
Practical Guide to Vegetable Oil Processing, 2nd. Ed., Elsevier Press/AOCS Press; Johnson, L. A., White, P. J., Galloway, R., Soybean Chemistry, Processing, and Utilization, AOCS Press.
Typical Fatty Acid Composition of Modified Composition Oils (Weight %)*

## Slide 35: Modified Composition are Also “Mortal” Like the Garden Variety Oils
The oils are still susceptible to Hydrolysis like all Garden Variety Oils
The oils still degrade under abusive frying condition
Thus, the refined, bleached and deodorized (RBD) oils from the Modified Composition Oilseeds still need to meet the Finished Oil Specifications, shown in Slide #36.
“HO” oils demonstrate less polymers in fryers

## Slide 36
Recommended Quality Parameters for Frying Oils
Analysis | Desired Level | Maximum Level | AOCS Method
Free fatty acid, FFA, % | 0.03 | 0.05 | Ca 5a-40
Peroxide Value, PV, meq /kg | <0.5 | 1.0 | Cd-8b-90
Para Anisidine value, pAV, AVU unit | <3.0 | 5.0 | Cd-18-90
Conjugated dienes, % | Trace | <0.5 | Th-1a-64
Polar compounds, % | <2.0 | <4.0 | Cd-20-91
Polymers, % | <0.5 | <1.5 | Cd-22-91
Phosphorus, parts per million, PPM | <0.5 | <1.0 | Ca-12b-92
Iron, Fe, parts per million, PPM | <0.1 | <0.3 | Ca-18b-91
Calcium, Ca, parts per million, PPM | <0.2 | <0.5 | Ca-15b-97
Magnesium, Mg, parts per million, PPM | Trace | <0.5 | Ca-15b-97
Monoglycerides, % | ND | Trace | Cd-11b-91 Cd-11b-96
Diglycerides**, % | <0.5 | <1.0 | Cd-11b-91 Cd-11b-96
** Commercial palm oil may contain 5-11% diglycerides

## Slide 37: Oil Filtration
Oil filtration is essential in frying
Oil filtration:
  Removes suspended crumbs generated in frying
  Reduce and remove oil decomposition products
  Can improve product taste, flavor, appearance and even shelf life

## Slide 38: Types of Filtration
Passive Filters
Passive filters are those simply remove suspended materials in the oil
Active Filters
Active filters are those where the oil impurities are also reduced via physical as well as chemical reactions in addition to the removal of the suspended materials in the oil

## Slide 39: Examples of Passive & Active Filters
Most commonly used passive filters are:
  Paper
  Fine mesh screens (cloth or metal)
Paper filter simply retains most of the suspended material in the oil. They do not remove impurities from the oil
Examples of active filters are:
  Paper with reactants /adsorbents sprinkled on it
  Paper impregnated with adsorbents
  Pads impregnated with reactants
  Powders containing reactants and adsorbents. The powder is filtered out with paper
  Pads impregnated with adsorbents

## Slide 40: Active Filters
Active filters remove or reduce the oil breakdown compounds via:
Physical Means-Where the impurities in the oil containing electronic charges are attracted and attached to the active sites of the adsorbents used in filtration
Chemical means where the FFA in the fryer oil is reacted with an alkali metal. The FFA is reduced but this leads to the formation of soap that remains in the oil.
This reduces fry life of the oil

## Slide 41: Active Filter Treatment in Industrial Frying
Use of adsorbent powder
Use of pads containing adsorbents

## Slide 42: Use of Adsorbent Powder (Example:Dalsorb-Treatment)

## Slide 43: Schematic Diagram for FM-4 (Filtercorp System)

## Slide 44: FM-4 Filter from Filtercorp

## Slide 45: Reloading the Filter-Module

## Slide 46: Concluding Remarks
Oil degrade during frying due to:
  Hydrolysis
  Oxidation
  Thermal Degradation
For better product shelf life, the oil quality must be managed in frying
Modified Composition Oils exhibit higher oxidative Stability than Garden variety Oils
All oils must meet the RBD Standards shown in Slide #35
Even the Modified Composition Oils cannot be used under ‘Abusive” frying conditions (Slide #27)
Fryer oil must be filtered
Active Filters remove oil impurities and extend fry-life of the oil

## Slide 47: Recommendations
Develop and implement:
Raw Material Quality Management Program:
  Raw material specifications
  Raw material receiving and storage procedure (Temp., Humidity, Storage Time, etc.)
Oil Quality Management Program:
  Fresh oil quality specification
  Oil receiving and storage procedure
  In-process oil quality standards and management procedure
  Used oil quality standard and management procedure
  Fryer start up and shut down procedures
  Temporary fryer shut down procedure
Product Quality Management Procedure:
  Finished product standards
  Trouble shooting procedure for quality deviations
  Storage and distribution procedure

## Slide 48: Acknowledgement
I wish to extend my sincere appreciation to TCI for inviting me to present this paper
I also wish to extend my appreciation to FiltercorpNA® for supporting my trip.